## Slide 1: PRACTICE QUESTIONS

## Slide 2: Q1: Draw CFG for the following program and derive data flow testing paths and no. of test cases required
main()
{
int work;
double payment= 0;
Scanf(“%d”, work);
if(work>0){
payment=40;
If(work>20)
{
If(work<=30)
payment=payment+(work-25)*0.5;
else
{
payment= payment+50+(work -30)*0.1;
If(payment>=3000)
payment=payment*0.9;
}
}
}
printf(“Final payment”, payment);
}

## Slide 3: Q2: Consider a project with the following functional units:
Number of user inputs= 50
Number of user outputs= 40
Number of user inquiries= 35
Number of files=06
Number of external interfaces=04
Assume all complexity adjustment factors and weighting factors are average. Compute Function points for the project.

## Slide 4: Q3: An application has the following:
10 low external inputs, 12 high external outputs, 20 low internal logical files, 15 high external interface files, 12 average external inequires, and a value of complexity adjustment factor of 1.10.
What are the unadjusted and adjusted function point counts.

## Slide 5: Q4: Consider a project with the following parameters
i) External inputs:
10 with low complexity
15 with average complexity
17 with high complexity
ii) External Outputs
6 with low complexity
13 with high complexity
iii) External inquiries:
3 with low complexity
4 with average complexity
2 with high complexity
iv) Internal Logical files:
2 with average complexity
1 with high complexity
v) External Interface Files:
A) 9 with low complexity
In addition to above, system requires
Significant data communication
Performance is very critical
Designed code may be moderately reusable
System is not designed for multiple installations in different organisations.
Other complexity adjustment factors are treated as average. Compute the Function points for the project

## Slide 6: Q5:Suppose that a project was estimated to be 400 KLOC. Calculate the effort and development time for each of the 3 modes: Organic, Semidetached and Embedded. Q6: A project size of 200 KLOC is to be developed. Software development team has average experience on similar type of projects. The project schedule is not very tight. Calculate the effort, development time, average staff size and productivity of the project.